Figure 1: Global view of Tingo Pucara surrounding relief*

* Source Document 507, 2008

|  | Flow | Quality | Remarks |
| --- | --- | --- | --- |
| QUILOA SOURCE | ~3.32 l/s |  | No electric cable |
| SECONDARY SOURCE | ~0.23 l/s |  | On the edge of a cliff |

*Source Document 507, 2008

Water Quality from Document 522, 2009

| Parameters | Guideline Value | Primary Water Source | Tap Water from Other community | Biosand Effluent |
| --- | --- | --- | --- | --- |
| Nitrate | 50 mg/L | 1 mg/L | 10 mg/L | 10 mg/L |
| Nitrite | 3 mg/L | 0.25 mg/L | ~ 0 | ~ 0 |
| Chloride | 250 mg/L* | 500 mg/L** | 500 mg/L** | 500 mg/L ** |
| pH | 6.5 - 8.5* | 6.3 -6.5 | 6 | 9.5 (Influent 6 -6.5) |
| Hardness | Acceptance issue | 100 ppm (Soft) | 100 ppm (Soft) | 80 ppm (Soft) |
| Iron | 0.3 mg/L* | 0.01 ppm | N.A. | ~ 0 |
| Chlorine | 5 mg/L | N.A. | N.A. | N.A. |
| Coliform | 0/100 ml | N.D. | N.D. | N.D. |
| * No guideline values from WHO, but exceeding listed values are recommended for additional attention. |
| ** The testing kit seemed to show up wrong colors. |
| N.A. = Not analyzed. N.D. = Not detected. |
| Tap water was tested by Oswaldo's house, and the Biosand filter was at Agustin's house. |

# Text boxes

Quiloa Source

Tingo Pucara

Secondary Source

Pucara